## Slide 1
Telescope
Bridge 4
Abutment
Reading “A”
119.476
Concrete 117.700 O.S. Level
Soil 117.350
O.S. Level
2.126 m
1.776 m
Bridge 4
to soil
119.476
-117.350
= 2.126m
Bridge 4 to
concrete
119.476
-117.700
=1.776m
“B”= 1.776 + “A”
Calculate “B”
Concrete level from telescope sight line
= 1.776m
+ ………………………..“A” m
= ………………..………”B” m
Calculate “C”
Soil level from telescope sight line
= 2.126m
+………….….………”A” m
= ……………..……”C” m
“C” = 2.126 + “A”
Date amended
02/04/2020
Notes: - The required staff reading was calculated as 1.776 (“B”) + 1.632 (“A”) = 3.408.
Concrete height measurements after casting were:- .
3.405
3.402
3.405
3.416 offside next to wall
3.406 offside next to wall
This gives a worst error of 8 mm too low and 6mm too high on the positions measured on 12th March
Who……………………….
Sight line
Staff
Concrete 300mm thick
File:Surveying sheet for Swing bridge walls version 3 As built
O.S. Level
0.300m
Concrete Blinding 50mm thick
Concrete blinding 50mm thick
Notes: Wall base measured at 117.542 and 117.416 O.S. Concrete level raised 300 mm to support wall base